## Slide 1: S-Pen Detection System – Overview
End-to-end workflow of S-Pen detection using
- Camera (OpenCV)
- YOLO ML model
- Arduino trigger
- Orientation validation
- PASS/FAIL decision logic

## Slide 2: Problem Statement
Detect S-Pen correctly while avoiding:
- Wrong phone orientation
- Partial insertion
- False positives

## Slide 3: ML Pipeline Overview
1. Data collection
2. Annotation
3. Model training
4. Deployment
5. Real-time inference

## Slide 4: Why Trigger-Based Inference
Inference runs only when Arduino sends 1
Reduces CPU load
Improves reliability

## Slide 5: OpenCV Camera Basics
cap = cv2.VideoCapture(0)
ret, frame = cap.read()
Frames are passed to ML model

## Slide 6: YOLO Inference Flow
Frame → YOLO → Bounding boxes
Filter by class & confidence

## Slide 7: Orientation Problem
Pen detected even when phone flipped
Solution: mic/USB reference

## Slide 8: Template Matching Logic
Crop mic/USB once
cv2.matchTemplate()
LEFT = correct
RIGHT = wrong

## Slide 9: PASS / FAIL Logic
PASS if:
- Pen present
- Orientation correct
Else FAIL

## Slide 10: Arduino Integration
Input: Object presence
Output: Conveyor control

## Slide 11: GUI Responsibilities
Live feed
Status display
Serial handling
Operator control

## Slide 12: End-to-End Flow
Object → Trigger → Camera
→ ML → Orientation → Decision → Conveyor